## Slide 1
Kurt J. Marfurt (The University of Oklahoma)
Conditioning of Migrated, Stacked Data
Footprint Suppression
Seismic Attributes - from Interactive Interpretation to Machine Learning

## Slide 2
After this section you should be able to:
  Recognize the appearance of acquisition footprint and avoid interpreting it as signal
  Apply kx-ky and other filters to partially suppress periodic footprint
Data conditioning – Footprint suppression
Notes: A list of learner objectives for the section on seismic data conditioning.

## Slide 3: Causes of Acquisition Footprint
  Aliased backscattered noise, e.g. ground roll and low-velocity shallow diffractions
  Bin-to-bin variations in the distributions of offsets and azimuths that exacerbate AVO effects
  Obstacles causing deviations from the desired regular geometry
  Migration operator’s attempt to image steep dips with short horizontal wavenumbers

## Slide 4
CGG Veritas slip-sweep acquisition
CGG Veritas V1 acquisition
The best way to avoid footprint? Improve your survey design.
(CGG-Veritas ad. AAPG Explorer, July, 2009)
Impact of denser, single vibrators, vs. more widely separated vibrator arrays
4 sweeps per shot location
1 sweep per shot location. Double the shot lines!
Notes: Recently, several seismic acquisition companies have designed workflows that replace conventional vibrator arrays generating vertically stacked data with denser acquisition using single sweep vibrators. With concomitant deployment of wide-azimuth, denser geophone arrays, considerable improvement in data quality can be achieved within the same time frame at the same cost. The reason for the improvement is that much of our noise is not random, but rather coherent. Leakage of ground roll, airwaves, and other coherent noise cannot be suppressed through vertical stacking. By adding additional shot points, we exploit the fact the differences in moveout between reflections and diffractions of interest vs. coherent noise. The result is a decrease in acquisition footprint (and because the decreased bin size) increased lateral resolution. (The above advertisement from CCG-Veritas can be found in the July 2009 AAPG Explorer, page 17).

## Slide 5: Reducing acquisition footprint by reprocessing the original common shot gathers

## Slide 6
Original data. Note the E-W acquisition footprint
1272 ms
1332 ms
1316 ms
Amplitude
Coherence
(Chopra et al., 2002)
The next best way to avoid footprint? Improve your processing workflow.
Notes: Time slices, at t = 1.272, 1.316, and 1.332 s, through (a) a seismic data volume and (b) the corresponding coherence volume. The acquisition footprint does not impede our ability to interpret the original seismic amplitude data, but it is exacerbated by the coherence calculation, in which we see wide east-west and narrow north-south artifacts. After Chopra (2002).

## Slide 7
(Chopra et al., 2002)
1272 ms
1332 ms
1316 ms
Amplitude
Coherence
After trace balancing, statics, and improved velocity analysis
The next best way to avoid footprint? Improve your processing workflow.
Notes: The same data slices as those shown in the previous figure, but displayed here after additional seismic processing (balancing, statics, and improved velocity analysis) to minimize the acquisition footprint. Although the impact on the original seismic data is minimal, we now are able to discern minor faults (indicated by gray arrows) and possible stratigraphic features (indicated by white arrows) that previously were masked by the acquisition footprint. After Chopra (2002).

## Slide 8
(Famini et al, 2005)
Time = 0.940 s
Reduced footprint
The next best way to avoid footprint? Improve your processing workflow.
Vacuum Field, Delaware Basin
A processing workflow that minimizes footprint
Poor resolution
Poor resolution
Poor resolution
Reduced footprint
Notes: Comparison of a time slice, at 1.0 s, through coherence volumes generated for a survey from the Delaware Basin, New Mexico, USA. The coherence slice from original processing. After Famini (2005).

## Slide 9
Time = 0.940 s
(Famini et al, 2005)
Coherence on reprocessed data
Vacuum Field, Delaware Basin
Stronger footprint
Better resolution
Vacuum Field, Delaware Basin
A processing workflow that maximizes resolution
Better resolution
Better resolution
Stronger footprint
Notes: Comparison of a time slice, at 1.0 s, through coherence volumes generated for a survey from the Delaware Basin, New Mexico, USA. Coherence slice after careful reprocessing to improve lateral resolution. Note the trade-off between increased acquisition footprint in the northeast corner, indicated by the yellow arrow, and improved resolution in the Brushy Canyon slump features indicated by the green arrow. Unfortunately, in this example improving the lateral resolution of the geologic features of interest also exacerbated the acquisition footprint. After Famini (2005).

## Slide 10
If the acquisition geometry follows a pattern, acquisition footprint will have periodic components
The amplitude and location of these components will change with depth (and generally heal at greater depths)
If we know the acquisition program and processing workflow, we can predict what this pattern will be
Attributes exacerbate the impact of footprint
Attributes may therefore serve as a means of characterizing footprint, allowing us to model it without knowing the details of acquisition and processing
Observations

## Slide 11
Original data
(Drummond et al., 2001)
kx-ky filters based on knowledge of the acquisition and processing
Data after kx-ky notch filtering
Data after adaptive filtering
t = 3.2 s
kx
ky
Land data, Algeria
Notes: One of the first examples showing the advantage of kx-ky filtering of the migrated seismic data. The kx-ky pedestals were computed from knowledge of the source and receiver locations. Comparison of original data, data after kx-ky filter, and data after adaptive filtering. (After Drummond et al., 2001).

## Slide 12
Amplitude
Positive
Negative
0
A’
A
Time (s)
0.750
0.500
0.250
0.000
(Falconer and Marfurt, 2008)
Central Basin Platform, TX
Seismic
amplitude
A
A’
4 km
N
Footprint
Footprint
Signal
Signal
kx-ky pattern seen on seismic amplitude
Notes: (Left) A vertical slice and (Right) time slice at t=0.5 s through a seismic amplitude volume acquired over the Central Basin Platform of west Texas, Note the strong periodic acquisition footprint that contaminates the data. Careful examination of the vertical slice shows that this footprint correlates to the steeply dipping artifacts cutting across the reflection events of interest. Without further access to the data, the two most likely causes are migration operator aliasing and/or aliased ground roll and shallow diffractions that have leaked through the processi

## Slide 13
Sobel filter
similarity
Coherence
High
Low
Amplitude
Positive
Negative
0
A’
A
Time (s)
0.750
0.500
0.250
0.000
(Falconer and Marfurt, 2008)
A
A’
4 km
N
Footprint
Footprint
Signal
Signal
Can we use coherence to characterize the footprint pattern?
kx-ky pattern seen on seismic attributes
Central Basin Platform, TX
Notes: The same vertical section but now with a time slice at the same t=0.5 s level through the coherence (Sobel filter similarity) volume. Note the periodic pattern of the low coherence anomalies. Because coherence (and other attributes) are more sensitive to the footprint than the amplitude data, can we use it characterize the footprint pattern?

## Slide 14
-.02
.02
.01
-.01
.02
.01
-.01
-.02
0
kx (cycles/km)
0
ky (cycles/km)
(Falconer and Marfurt, 2008)
kx-ky magnitude spectrum of the seismic amplitude
Blurred pedestals
Reflector response
Seismic amplitude spectrum
Notes: In the next three figures, I present a footprint suppression workflow that can often (but not always!) be successfully applied to migrated data. Since the data were acquired using orthogonal shot and receiver lines, the footprint also has an orthogonal pattern. This pattern is quite visible in the kx-ky magnitude spectrum of the seismic amplitude data.

## Slide 15
Attribute spectrum
-.02
.02
.01
-.01
.02
.01
-.01
-.02
0
kx (cycles/km)
0
ky (cycles/km)
(Falconer and Marfurt, 2008)
kx-ky magnitude spectrum of the Sobel filter similarity (coherence)
Focused pedestals
Smaller Reflector response
Notes: This periodic footprint pattern is exacerbated by the edge-sensitive attributes. The goal is to identify high magnitude kx-ky noise components. The most direct workflow is to construct a suite of notches based on these pedestals, apply it to the magnitude spectrum of the seismic amplitude data shown in the previous figure, and then reconstruct the data.

## Slide 16
-.02
.02
.01
-.01
.02
.01
-.01
-.02
0
kx (cycles/km)
0
ky (cycles/km)
(Falconer and Marfurt, 2008)
kx-ky magnitude spectrum after application of an LoG sharpening filter
Sharpened attribute spectrum
Using Laplacian of a Gaussian (LoG)
Sharpened pedestals
Muted reflector response
Notes: A pitfall in kx-ky filtering is that we may reject desired signal as well as undesired noise. For this reason, the noise characterization should be as focused as possible. By applying a Laplacian of a Gaussian filter to the previous image, we can sharpen the location of the footprint pedestals. Care must be taken near low wavenumber components about kx=ky=0. For example coherence anomalies associated with unconformities and other stratigraphic features that are nearly horizontal will give rise to low wavenumber anomalies. In this example, we have applied a simple mute to the lowest wavenumber components. The footprint at these components will therefore not be addressed.
In the next steps, we will apply the picked pedestals to the original seismic amplitude kx-ky magnitude spectrum, reconstruct a model of the seismic amplitude noise, and adaptively subtract it from the the original x,y amplitude data.

## Slide 17
Amplitude
α2
α1
α3
distance
A
A’
α6
α5
α4
L
L
L
αk
Six 1D weighting functions approximating a continuous curve (each with a coefficient αk )
A 2D weighting function
(Falconer and Marfurt, 2008)
Modeling the seismic noise using 1D and 2D basis functions
Notes: This image shows how one can represent a curved pink line by the linear combination of sixed (dotted yellow) raised cosine basis functions which add to give the dashed yellow line. The mathematical problem is then to estimate the six coefficients, alpha, that represent the hundreds of data measurements on the pink line. For footprint suppression, we will model the noise response using 2D Gaussian basis functions, as shown in the lower left of this figure.

## Slide 18
data
noise estimate
α1
α2
α3
α4
α5
α6
α7
α8
α9
α10
α11
α12
α13
α14
α15
α16
α17
α18
α19
α20
α21
α22
α23
α24
α25
α26
α27
α28
α29
α30
noise fit to data
(Falconer and Marfurt, 2008)
Modeling the seismic noise using 2D basis functions
Notes: In this workflow, the basis functions consist of 36 2D raised cosines. These raised cosines are cross-correlated with the noise prediction obtained by the inverse kx-ky filter applied to the amplitude data represented by the previously defined noise filter mask. The resulting image is least-squares fit to the original amplitude time slice. Notice that it has a basket-weave pattern.

## Slide 19
Details of adaptive subtraction
The goal of the algorithm is to minimize the error between the original data, d, and a weighted version of the noise, n:
where w are 2D weighting functions, and αk is the amplitude of the kth control point.
Solving for α, we obtain:
where the small value β prevents division by zero in dead-trace areas.
(Falconer and Marfurt, 2008)
Notes: Here is the arithmetic for those of you interested. dij is an input amplitude datum, wijk is the jth raised cosine, and nij is the modeled noise after applying the mask to the kx-ky transformed amplitude data and reverse transforming back to x,y space.

## Slide 20
Generate attributes
sensitive to footprint
Apply vertical median filter
to enhance footprint
and suppress stratigraphic
features
For each time slice,
characterize footprint
in kx-ky space
(threshold the peaks)
Mask amplitude data
Generate smooth pedestal
filters (mask in kx-ky space) that best represent attribute footprint
Recompute attributes
for QC
Adaptively subtract noise
components from
original data
Amplitude
data
Footprint-
contaminated
attributes
Footprint
kx-ky mask
Modeled noise
Filtered
data
Footprint- free
attributes
kx-ky transform
amplitude data
Reverse kx-ky
transform
(Falconer and Marfurt, 2008)
Notes: Here is the workflow. It looks complicated, but thus is the world of seismic processing.

## Slide 21
t=600 ms:
San Andres level
t=500 ms
N
12,000 ft
Time slices through Sobel filter similarity (coherence)
Sobel Attribute
High
Low
Core
(Falconer and Marfurt, 2008)
Application to a Central Basin Platform survey (west Texas)
Notes: Images at t=500 and 600 ms. One of the targets is at the San Andres level. Footprint is strong at 500 ms, a little weaker at 600 ms, but strong enough to mask what we think are karst collapse features. The red dot shows the well location on the following slide.

## Slide 22
Karst
Karst
Karst
Top G3
Top G4
1200
1100
1150
Karst
Karst
Depth (m)
0.6 m
Anhydrite
Karst forms the updip seal
(Falconer and Marfurt, 2008)
Notes: Note the anhydrite-filled karst seen in the well.

## Slide 23
Footprint
Footprint
Footprint
Amplitude
Positive
Negative
0
Application to a Central Basin Platform survey (west Texas)
Time slices through migrated amplitude data volume
N
12,000 ft
(Falconer and Marfurt, 2008)
t=600 ms:
San Andres level
t=500 ms
Notes: These time slices show footprint on the original amplitude data. One of the exploration targets is the San Andres level near t=600 ms, where we see strong footprint.

## Slide 24
x
=
x
=
Noise predicted from mask
Weights calculated from adaptive subtraction
Weighted noise to be subtracted from seismic data
(Falconer and Marfurt, 2008)
Details
t=600 ms:
San Andres level
t=500 ms
Notes: The top row of images at t=500 ms and the bottom row of images at t=600 ms shows on the left panels the noise predicted by applying the attribute-derived noise mask to kx-ky of the amplitude data and inverse transforming to x-y space to obtain a noise estimate. Note that noise is predicted even in the dead trace areas. The central panels show the weights applied to the predicted noise, while the right panels show the least-squares (adaptively) fit of the noise to the original amplitude data. This noise estimate will be simply subtracted from the original data.

## Slide 25
N
12,000 ft
Footprint
Footprint
Footprint
Footprint
(Falconer and Marfurt, 2008)
t=600 ms:
San Andres level
t=500 ms
Before footprint suppression
Amplitude
Positive
Negative
0
Notes: The two amplitude slices before footprint suppression.

## Slide 26
N
12,000 ft
(Falconer and Marfurt, 2008)
After footprint suppression
t=600 ms:
San Andres level
t=500 ms
Amplitude
Positive
Negative
0
Notes: The same two amplitude slices after footprint suppression.

## Slide 27
N
12,000 ft
Sobel Filter
High
Low
footprint
footprint
footprint
footprint
geology?
(Falconer and Marfurt, 2008)
Before footprint suppression
t=600 ms:
San Andres level
t=500 ms
Notes: The two attribute slices computed from the seismic amplitude data before footprint suppression.

## Slide 28
N
12,000 ft
Sobel Attribute
High
Low
(Falconer and Marfurt, 2008)
Before footprint suppression
t=600 ms:
San Andres level
t=500 ms
Notes: The two attribute slices computed from the seismic amplitude data before footprint suppression. The insert on the left shows the target karsted area. What is karst and what is footprint?

## Slide 29
N
12,000 ft
(Falconer and Marfurt, 2008)
Sobel Attribute
High
Low
After footprint suppression
t=600 ms:
San Andres level
t=500 ms
Notes: The two attribute slices computed from the seismic amplitude data after footprint suppression. The insert on the left appears more geological. While we can not assure that there is no footprint remaining in these images, we are confident that at least the periodic components of noise have been removed.

## Slide 30
Pitfalls in kx-ky footprint suppression
A
A’
Time slice through “noise” at t = 0.5 s
(Falconer and Marfurt, 2008)
Notes: A pitfall arises when we have steep dip. In this image, the green arrow indicates signal associated with steep dips going into the Midland Basin.

## Slide 31
A’
A
0.4
0.5
0.6
0.3
Time (s)
A’
A
0.4
0.5
0.6
0.3
Time (s)
A’
A
0.4
0.5
0.6
0.3
Time (s)
“Noise”
Filtered data
Input data
(Falconer and Marfurt, 2008)
Pitfalls in kx-ky footprint suppression
Dipping reflectors
Dipping reflectors
Notes: Further inspection shows removal of steeply dipping migration artifacts, but also part of the steeply dipping reflectors. The kx-ky components of the steeply dipping reflectors overlaps with the kx-ky components of the noise and has been removed! Applying such a filter on flattened volumes would be a potential workaround.

## Slide 32: Alternative workflow examples: Footprint contamination on structural curvature
kx-ky filtering
workflow
Seismic
amplitude
Structure-
Oriented
filtered
volume
SOF filtering workflow
Positive
Negative
Amplitude
t=0.8 s
(Davogustto, 2011)
Notes: One can cascade filters. Here, Davogustto has followed kx-ky filtering with structure-oriented filtering.

## Slide 33
kx-ky filtering
workflow
Seismic
amplitude
Structure-
Oriented
filtered
volume
SOF filtering workflow
Positive
Negative
Most positive structural
principal curvature
0
t=0.8 s
Alternative workflow examples: Footprint contamination on structural curvature
(Davogustto, 2011)
Notes: While not perfect, the resulting curvature images now lack much of the east-west and north-south artifacts seen on the original data. The NW-SW trending artifacts (green arrow) are still suspicious.

## Slide 34: Original Amplitude Slice (t= 0.45 s)
2 mi
0
Positive
Negative
Amplitude
Footprint suppression using kx-ky filters
(Alali et al., 2016)
Notes: (a) Time slice at t = 0.450 s through a seismic data volume acquired over Vacuum Field, NM, USA in the late 1990s. This part of the Delaware Basin has multiple objectives, with the shallow Yates horizon strongly contaminated by north-south and east-west acquisition footprint. The footprint heals with depth but still contaminates impedance and other attributes necessary for quantitative interpretation. (b) Corresponding time slice through the coherence volume. Coherence exacerbates the footprint, thereby making it a noise characterization tool. (c) Because it has little to do with the reflectivity, footprint varies slowly in the vertical direction, with the major change healing with depth due to an increase in fold and a decrease in sensitivity to velocities. If the lateral variation in the overburden velocity is smooth, the pattern persists but is slowly warped. These patterns allow one to “enhance” the footprint artifacts by applying a ±100 ms median filter to the coherence volume. Seismic data courtesy of Marathon Oil Co.. After Figure 1 of Alali et al. (2016). Used by permission.

## Slide 35: Coherence Slice (t= 0.45 s)
1.0
0.0
Coherence
2 mi
Footprint suppression using kx-ky filters
(Alali et al., 2016)

## Slide 36: Slice through median-filtered coherence (t= 0.45 s)
2 mi
1.0
0.0
Coherence
Footprint suppression using kx-ky filters
(Alali et al., 2016)

## Slide 37: kx-ky transforms
of amplitude slice
of filtered coherence slice
(Alali et al., 2016)
kx (cycles/kft)
-25
+25
0
kx (cycles/kft)
-25
+25
0
ky (cycles/kft)
-25
+25
0
Maximum
0
Magnitude
Notes: Time slices at t = 0.45 s through the kx-ky transform of (a) the seismic amplitude volume, and (b) the coherence volume after application of a vertical median filter to enhance footprint. Since coherence sharpens edges it exhibits a much stronger response at shorter wavelengths than the amplitude data. Time slices through seismic amplitude exhibit a “sliced onion appearance” which may be periodic. Because coherence is computed along structural dip it does not exhibit this periodicity. A single, planar fault would be represented by a weak line in the kx-ky domain. Periodic footprint anomalies appear as a suite of strong points. The high magnitude blob about kx=0 and ky=0 corresponds to smoothly varying amplitudes in (a) and coherence in (b) associated with flatter reflectors. (c) Application of a Laplacian of a Gaussian filter to coherence results in a sharper kx-ky amenable to construction of a kx-ky pedestal filter. Seismic data courtesy of Marathon Oil Co. After Figure 2 of Alali et al. (2016). Used by permission.

## Slide 38: kx-ky transforms
(Alali et al., 2016)
of amplitude slice
of Laplacian of a Gaussian applied to
filtered coherence slice
kx (cycles/kft)
-25
+25
0
kx (cycles/kft)
-25
+25
0
ky (cycles/kft)
-25
+25
0
Maximum
0
Magnitude
Build a pedestal filter at each location

## Slide 39
0
Positive
Negative
Amplitude
Rejected Noise (t= 0.45 s)
2 mi
Footprint suppression using kx-ky filters
(Alali et al., 2016)
Notes: Time slice at t = 0.45 s through (a) the rejected noise obtained using the pedestal filter shown in Figure 15c. (b) Filtered data obtained by adaptably subtracting the data shown in (b) from the original data shown in Figure 14a. (c) An alternative filtering approach based on 2D continuous wavelet transforms in the (x, kx, y, ky) domain. Seismic data courtesy of Marathon Oil Co.. (c) After Figure 10 of Alali et al. (2016). Used by permission.

## Slide 40
Amplitude Slice after Footprint Suppression (t= 0.45 s)
2 mi
0
Positive
Negative
Amplitude
Footprint suppression using kx-ky filters
(Alali et al., 2016)

## Slide 41: Amplitude Slice after Footprint Suppression (t= 0.45 s)
2 mi
0
Positive
Negative
Amplitude
Footprint suppression using 2D CWTs
(Alali et al., 2016)
2 mi

## Slide 42
N
4 km
Before footprint suppression using x-y wavelet transforms
(Cvetkovic et al., 2008)
Footprint suppression using 2D CWTs
(Chicontepec Basin)
Notes: In this example Cvetkovic et al. (2007) applied 2D x-y wavelet transforms to the data. This 2D transform is basically a space-variant kx-ky transform.

## Slide 43
b)
N
4 km
After footprint suppression
(Cvetkovic et al., 2008)
Footprint suppression using 2D CWTs
(Chicontepec Basin)
Notes: High amplitude noise components were muted and the data reconstruction, resulting in very nice lineament preservation.

## Slide 44
In Summary:
Periodic acquisition programs often generate periodic acquisition footprint. For reasonably flat overburden, the periodic pattern can be attenuated through kx-ky filtering
The 2D CWT can adapt to footprint that changes pattern due to the velocity overburden or due to different acquisition patterns seen in merged surveys,
Dense acquisition is the best way to avoid acquisition footprint. For wide azimuth land acquisition, increasing the number of traces per km2 by a factor of four does not increase the cost of acquisition by four
5D interpolation is a partial solution to footprint prior to impedance inversion; however, edges in the data are often smeared
Post Migration Poststack Data Conditioning
Notes: Summary comments on post-migration data conditioning of post-stack data