## Slide 1
Image Enhancement of Faults
Kurt J. Marfurt (The University of Oklahoma)
Seismic Attributes - from Interactive Interpretation to Machine Learning

## Slide 2
After this section you should be able to:
  Apply simple filters to coherence or other edge-sensitive attributes enhance faults and suppress stratigraphic features parallel to stratigraphy
  Estimate the orientation, and for some algorithms, the heave of individual faults
Image enhancement of faults
Notes: Learner objectives for this lecture. Conventional seismic processing and data conditioning are applied to the seismic amplitude data volumes. In this section we apply image processing filters to seismic attribute volumes to smooth or sharpen faults.

## Slide 3
Ant-tracking
(Marfurt, 2018)
Notes: While Marfurt is not a proven leader of men, he has been known to be followed by children, dogs, and even large insects (such as his graduate student apartment in New York City).

## Slide 4: Swarm intelligence and mapping faults
Ants that don’t find sugar, die!
Ants are scattered randomly over the area to be explored. Each ant can make 6*10 steps.
Ants that do find sugar, drop pheromones
X
X
X
(Marfurt, 2018)
Notes: Illustration of swarm intelligence such as implemented in Schlumberger’s ant-tracker software. An edge-sensitive attribute such as coherence is considered to be sugar. The edges may be smeared laterally and disjoint vertically. In the first step, a suite of ants are dropped into the image. Each ant has sufficient energy to take n random steps. If the ant does not find sugar (a coherence anomaly), she dies. However those ants who do find sugar can not only take more steps, but leave pheromones (purple stains) indicating the trail they have followed, leading other ants to the sugar. (Photos by the author).

## Slide 5: Swarm intelligence and mapping faults
The process continues until the trail is well marked
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
More ants arrive. Those who follow the pheromones and find sugar, live and leave more pheromones. Those that don’t die after n steps.
(Marfurt, 2018)
Notes: The process continues with more ants being drawn to the sugar. Those that wander off, die, and leave minimal pheromones behind, those that follow the pheromones and find more sugar continue the process, thereby mapping out a distinct trail. (Photos by the author)

## Slide 6
Ant-tracking
(Pedersen et al., 2002)
Notes: (a)Two ants start at the same time at the nest. (b) The ant choosing the shorter path will arrive at the nest before the ant choosing the longer path. The shorter path will thus be marked with more pheromone than the longer path, and hence the next ant, influenced by the pheromone, is more likely to choose the shorter path.
By encoding fault properties expectations as behavior of intelligent software agents, we are able to enhance and extract fault-like responses in the attribute. An agent will act very similar to an ant in the foraging situation described above, by making decisions based on its pre-coded behavior and emitting “electronic pheromone” along its trail. The idea is to distribute a large number of agents in the volume, and let each agent move along what appears to be a fault surface while emitting pheromone.
Agents deployed at points where there is no surface, only unstructured noise, or where there is a surface which does not fulfill the conditions for a fault (e.g. remains of a reflector), will be terminated shortly or immediately after their deployment. Agents deployed on a fault, on the other hand, should be able to trace the fault surface for a while upon being terminated. We expect that surfaces fulfilling our expectations for faults will be traced by many agents deployed at different positions in the volume, and hence be strongly marked by “pheromone”. Noise and surfaces unlikely to be faults should be unmarked or weakly marked, and will be removed by thresholding

## Slide 7
Fault enhancement using ant-tracking
(Silva et al., 2005)
Notes: Original discontinuity image using a coherence (variance) algorithm and fault enhancement after ant-tracking. (After Silva et al., 2005).

## Slide 8
Digitize seed points
Extract fault patches
Merge
Convert to pillars or fault segments
Ant-tracking workflow
(Petrel documentation)
Notes: Software workflow to convert enhanced faults from ant-tracking into seismic objects. In turn, these objects are converted to pillars or fault segments.

## Slide 9
All fault patches extracted using
ant-tracking
(Silva et al., 2005)
Ant-tracking workflow
Notes: Fault Surfaces created during the Ant Tracking attribute calculation. (After Silva et al., 2005).

## Slide 10
Fault patch artifacts associated with acquisition footprint
(Silva et al., 2005)
Ant-tracking workflow
Notes: Left: Fault surfaces oriented along inline direction (effect of seismic acquisition/processing). Right: Stereonet diagram used to filter fault surfaces aligned with inline and crossline directions. Each point represents one fault surface and those plotted in the grayed areas were filtered out. (After Silva et al., 2005).
Stereo net with projected fault orientations. Fault systems can be seen as dense clusters on the net. The azimuth of the normal can be read along the perimeter and the dip is the distance from the center. The normal of horizontal surface would be plotted in the center of the net, and a vertical surface would be plotted somewhere along the perimeter depending on its strike.

## Slide 11
The filtered fault sets
Ant-tracking workflow
(Silva et al., 2005)
Notes: Fault Surfaces created during the Ant Tracking attribute calculation. (After Silva et al., 2005).

## Slide 12: Ant-tracking applied to volumetric curvature
(Baruch et al., 2009)
Notes: Ant-tracking is an image processing algorithm rather than a fault-detection algorithm and thus can track more than faults. In this case it is used to track axial planes mapped by most-positive curvature. Horizon slice along the top basement through the most-positive curvature volume for a survey in the Fort Worth Basin and its corresponding rose diagram. (Bottom Left) Image enhancement using the ant-tracking algorithm and (Bottom right) superposition of curvature and ant-tracking of the curvature. (After Baruch et al., 2009).

## Slide 13: Estimating fault probability, heave, and throw
Computing fault images,
Constructing fault samples,
Constructing fault surfaces,
Estimating fault dip slips,
Unfaulting the seismic image to assess the accuracy of those slip vectors.
(Wu and Hale, 2016)
Notes: (a) Fault dip slip is a vector representing displacement in the dip direction, of the hanging wall side of a fault surface relative to the footwall side. Fault throw is the vertical component of the slip. Fault strike and dip angles with corresponding unit vectors are defined in panel (b).

## Slide 14: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Interpreted faults
Fault likelihood
Problems with crossing faults and holes
Notes: (Left) Seismic amplitude with interpreted faults. (Center) A fault likelihood volume computed using prediction error filtering. (Right) Skeletonized faults color-coded by fault-likelihood. (After Wu and Hale, 2016).

## Slide 15: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Fault squares
Linked fault squares
Filling in the holes
Notes: (a) Every voxel is represented by a rectangular surface represented by its fault likelihood, strike, and dip. (b) Links are then built among consistent fault samples, where each set of linked fault samples now appear opaque. (c) Fault samples displayed as larger overlapping squares.

## Slide 16: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Fault squares
Linked fault squares
Filling in the holes
Notes: (a) Close-up view of a subset of fault samples from the previous image. (b) Links built among nearby fault samples form three sets of linked samples, which represent three fault surfaces (or patches). Near the intersection of faults F-A and F-B, fault F-A is separated into two independent patches, and fault F-B has a hole. (c) New fault samples (colored with yellow and blue) are created to merge the fault patches and fill the hole to construct more complete intersecting fault surfaces.

## Slide 17: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Fault likelihood
Structure-oriented filtered volume
Notes: Linked fault samples in Figure 6c can be displayed as a fault likelihood image (with mostly zeros) overlaid with the seismic image in panel (a). Compared to the thinned fault likelihood image in Figure 5a, spurious fault samples have been removed. New fault samples are created at the intersection (dashed white circle) of faults A and B when constructing surfaces. This fault image is used to constrain a structure-oriented smoothing filter so that it smooths the seismic image along structures but not across the faults as shown in panel (b).
Figure 9. (a) Fault surfaces and fault throws for a 3D seismic image (b) before and (c) after unfaulting. In all image slices, reflectors are more continuous after unfaulting.

## Slide 18: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Removed fault displacement
Fault likelihood
Notes: Fault surfaces and fault throws for a 3D seismic image (Left) before and (Right) after unfaulting. In all image slices, reflectors are more continuous after unfaulting.

## Slide 19: Fault likelihood using predictive error filtering
(Wu and Hale, 2016)
Notes: 1.From this 3D seismic image, images of fault likelihood, strike, and dip are first computed by scanning over a range of possible strikes and dips with a semblance-based filter that highlights locally planar discontinuities.
2.These three fault images are then represented by fault samples, which are displayed as squares oriented by strikes and dips and colored by fault likelihood in the upper right panel of Figure 10a. Remember that each fault sample corresponds to a seismic image sample in the sampling grid of the seismic image; therefore, the same fault samples can be displayed as a fault likelihood image overlaid with the seismic image slices shown in Figure 10a.
3. The oriented fault samples are then linked to form fault surfaces, displayed in the upper right panel of Figure 10b. Many of these fault surfaces intersect each other, and the differences in strikes for these intersecting faults are approximately 60°. These fault surfaces are really just sets of linked fault samples located within the sampling grid of the seismic image; they appear as surfaces only because the squares representing the fault samples are displayed with sizes large enough to overlap with each other. These linked fault samples can also be displayed as a fault likelihood image overlaid with the seismic image in Figure 10b. In the constant-time slice, we observe complicated intersections among the extracted fault surfaces. Compared to the three slices in Figure 10a, some fault samples are removed when constructing surfaces because they cannot be linked to form surfaces with significant sizes. In this example, we discarded fault surfaces with fewer than 2000 samples. In addition, new fault samples are created to fill holes that occur where faults intersect.
4. These fault surfaces of linked fault samples are further used to estimate fault dip slips. Fault throws (vertical component of slips) are displayed on fault surfaces in the upper right panel of Figure 11. After estimating fault slips, the number of fault surfaces is reduced because we keep only fault surfaces for which dip slips are significant. Again, each fault sample in a fault surface corresponds to exactly one sample of the 3D seismic image, so fault throws can be displayed as a 3D image overlaid with the seismic image as in Figure 11a.
5. Using the estimated fault dip slip vectors, the seismic image can be unfaulted as shown in Figure 11b. In the unfaulted image, seismic reflectors in all image slices are more continuous than those in the original image slices shown in Figure 11a. For the fault with large slips highlighted by the red arrow in Figure 11a, footwall and hanging wall sides are moved significantly to align the reflectors on these opposite sides, as shown in Figure 11b.

## Slide 20
1. Coherence computation
2. Suppression of horizontal discontinuities
0.0
4.0
Time (s)
(Barnes, 2006)
3. Image dilation
4. Image erosion.
5. Merge with seismic in workstation
Image enhancement for fault extraction
Vertical slices
5 km
G
G
Notes: Vertical slices through (a) a seismic volume and (b) the corresponding discontinuity volume, for a survey acquired in southern Louisiana, USA. The data are courtesy of Seitel, and the attribute analysis is courtesy of Landmark Graphics. The results of successive filtering of the discontinuity volume shown on the vertical slice displayed in the animation, (a) after suppression of horizontal discontinuities, (b) after image dilation, and (c) after image erosion. (d) A composite image of discontinuity and seismic data. After Barnes (2005).

## Slide 21
(Barnes, 2006)
Image enhancement for fault extraction
1. Coherence computation
2. Suppression of horizontal discontinuities
3. Image dilation
4. Image erosion.
G
5. Merge with seismic in workstation
5 km
G
Time slices
Notes: a) A time slice, at t = 3.000 s, through the seismic data and (b) the corresponding time slice through the discontinuity volume computed from the survey shown in Figure 5.62. The data are courtesy of Seitel, and the attribute analysis is courtesy of Landmark Graphics. After Barnes (2005).
The results of successive filtering of the discontinuity volume shown on the time slice at t = 3.000 s in Figure 5.63b, (a) after suppression of horizontal discontinuities, (b) after image dilation, and (c) after image erosion. (d) A composite image of discontinuity and seismic data. After Barnes (2005).

## Slide 22: Fault Enhancement using a directional Laplacian of a Gaussian
Compute a volumetric attribute sensitive to faults or axial planes
Extract a spherical analysis window about each voxel
Compute eigenvectors and eigenvalues of the second moment tensor
Smooth parallel to the fault using a rotated Gaussian
Sharpen perpendicular to the fault using a direction Laplacian of a Gaussian
(Optionally) apply a filter to enhance or reject features parallel or perpendicular to structural dip
Co-render sharpened planar feature with its dip magnitude and dip azimuth
Notes: Workflow to enhance faults based on a directional Laplacian of a Gaussian

## Slide 23: Dynamics of an asteroid
v1
v2
v3
(https://svs.gsfc.nasa.gov/2061)
Center of mass, μ:
Inertia tensor, I:
Principal axes of inertia tensor, vn:
Notes: The 2nd moment tensors allow us to compute the axes and moments of inertia. In this image from NASA, the asteroid can rotate most easily about axis v(1), next easiest about axis v(2), and hardest about axis v(3). These three axes are the eigenvalues of the 2nd moment tensor A. (Video and image from https://svs.gsfc.nasa.gov/2061)

## Slide 24: Dynamics of a cloud of energy-weighted fault probability anomalies, ep≡e(1-c)
Center of mass, μ:
Inertia tensor, I:
Principal axes of inertia tensor, vn:
1 km
0.5 s
0.0
0.7
Probability
Notes: A cloud of fault probability (defined as 1-coherence) voxels. At any voxel, we define an ellipsoidal analysis window, compute its center of mass (probability) and inertia tensor. Where a fault is present, the v1 and v2 eigenvectors will align with the local fault plane. The v3 eigenvector will be perpendicular to the fault plane. (Data from the Great South Basin, courtesy of NZP&M).

## Slide 25: Edge enhancement filters applied to a photo
Original
Gaussian
Laplacian
Laplacian of Gaussian
(Marfurt, 2018)
Notes: Edge enhancement filters are familiar to anyone who ones a digital camera, with one of the most common being a Laplacian filter. Unfortunately, the Laplacian not only enhances edges, it also enhances point noise, increasing the contribution of the shortest wavelengths. In other cases, one may wish to blur a photo, thereby removing the wrinkles in your face. In this case, one can apply a Gaussian filter, decreasing the contribution of the shortest wavelengths. The Laplacian of a Gaussian filter cascades these two filters, first by filtering point noise but preserving continuous edges, then by enhancing those edges. Photo of the Tulsa Driller and filters courtesy of Abdulmohsen Alali, OU.

## Slide 26
Fault enhancement workflow
Seismic amplitude
Structure oriented filtering
Filtered seismic amplitude
Skeletonization & interpolation
Planar event probability
Planar event dip magnitude
Planar event dip azimuth
Skeletonized fault, stratigraphic edge, or unconformity
Attribute computation
Directional Laplacian of a Gaussian filtering
Coherence
Compute coherence or other edge attribute
Apply the LoG operator to enhance discontinuous anomalies
Compute fault dip magnitude, and dip azimuth based on second moment tensor method
Skeletonize the LoG -filtered images
Interpolate highest fault probability sample
(Qi et al., 2018)
Energy
Notes: We begin our workflow by using principal-component structure-oriented filtering to suppress both random and steeply dipping coherent noise. Then, we compute coherence attribute from the filtered seismic amplitude volumes. Next, we apply a directional LoG filter resulting in a smooth but somewhat blurred image. Finally, we skeletonize the LoG filtered image perpendicular to locally plan features.

## Slide 27: The 3D directional Laplacian of a Gaussian operator
(Marfurt, 2018)
Fault
v3
v2
v1
Positive
Negative
0
dLoG
(Marfurt, 2018)
Notes: Cartoon showing the directional Laplacian of a Gaussian operator applied to a candidate fault. The cloud of coherence values can be defined by the three eigenvectors. If there is a planar event, the first two eigenvalues, λ1 and λ2 are significantly greater than the third eigenvalue, λ3. In this case, eigenvectors v1 and v2 define the fault plane while eigenvector v3 defines its normal. The dLoG operator is constructed so that it sharpens in the v3 direction but smooths in the v1 and v2 directions. (Image courtesy of Gabriel Machado, OU).

## Slide 28
Hanging wall
Footwall
Fault strike
Fault throw
Dip magnitude θ
Dip azimuth
V3
N
E
Z
Normal fault
Notes: Cartoon of a normal fault defined by the eigenvector perpendicular to the fault plane. The projection of on the horizontal plane defines the “fault” dip azimuth , and angle between and the z-axis defines the “fault” dip magnitude.
Cartoon of a normal fault defined by the eigenvector 𝒗_𝟑 perpendicular to the fault plane. The projection of 𝒗_𝟑 on the horizontal plane defines the “fault” dip azimuth 𝜑, and angle between 𝒗_𝟑 and the z-axis defines the “fault” dip magnitude.

## Slide 29
Seismic amplitude
Iterative fault enhancement
(Machado et al., 2016)
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km
Amplitude
0
Negative
Positive
Notes: Application of iterative fault enhancement using a directional Laplacian of a Gaussian (dLoG) filter. Vertical slices through (a) seismic amplitude, (b) amplitude co-rendered with coherence, and (c) coherence using a five trace by one complex-sample analysis window. Yellow arrows in (c) indicate low coherence anomalies subparallel to stratigraphy. The same slice after applying the dLoG filter to the coherence volume (d) once, (e) twice, and (f) three times. Yellow arrows indicate the location of anomalies less than 25° to the structural reflector dip previously shown in (c) that have been filtered out. The “thicker” fault anomalies indicated by the magenta arrows are associated with faults that are subparallel rather than perpendicular to the orientation of the vertical slice. (g) co-rendered seismic amplitude shown in (a) with fault probability shown in (f). Compare to (b) to see the improvement. For animation of these seven figures please select DISC2018_Figure_30.video. (Data courtesy of NZPM; After Machado et al., 2016).

## Slide 30
Co-rendered seismic amplitude and original coherence
(5 traces, 1 complex sample)
Iterative fault enhancement
(Machado et al., 2016)
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km
Amplitude
0
Negative
Positive
Coherence
0.6
1.0
Opacity
100
0

## Slide 31
Original coherence
(5 traces, 1 complex sample)
Iterative fault enhancement
(Machado et al., 2016)
Coherence
0.6
1.0
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km

## Slide 32
Fault probability (iteration 1)
Iterative fault enhancement
(Machado et al., 2016)
Fault Probability
0.0
High
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km

## Slide 33
Iterative fault enhancement
(Machado et al., 2016)
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km
Fault Probability
0.0
High
Fault probability (iteration 2)

## Slide 34
Iterative fault enhancement
(Machado et al., 2016)
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km
Fault Probability
0.0
High
Fault probability (iteration 3)

## Slide 35
Co-rendered seismic amplitude and fault probability iteration 3
Iterative fault enhancement
(Machado et al., 2016)
1.2
1.4
1.6
1.8
2.0
2.2
Time (s)
1 km
Amplitude
0
Negative
Positive
Fault Probability
0.0
High
Opacity
100
0

## Slide 36
Corendered seismic amplitude and original coherence (5 traces, 1 complex sample)
A
A’
Iterative fault enhancement

## Slide 37
Corendered seismic amplitude and fault probability iteration 3
A
A’
Iterative fault enhancement

## Slide 38: Polygonal faulting (using a box probe)
N
Fault dip
magnitude
N
S
E
W
Fault dip
azimuth
Fault
dip azimuth
-180°
+180°
0°
Fault
dip magnitude
0°
90°
Opacity
100
0
Fault
probability
0
High
Opacity
100
0
(Machado et al., 2016)
Notes: 3D view of two vertical lines through the seismic amplitude volume plotted against a gray scale color bar, and a box probe through co-rendered fault dip azimuth and fault dip magnitude showing polygonal faulting. Hue indicates the azimuth perpendicular to the fault, saturation the dip magnitude and transparency the fault probability. In this manner, areas with a low probability of a fault are rendered transparent. To see animation through the volume, please select DISC2018_Figure3.32.video. (Data courtesy of NZPM: After Machado et al., 2016).

## Slide 39
(Qi et al., 2017)
n
Fault probability, fp
Is grid point a peak value?
Interpolate normal to fault plane
Distribute smax on hexahedron corners
Set s=0
Fault dip and azimuth, (θ,φ)
Skeletonized result, s
no
yes
Skeletonization
Notes: Given the dip and azimuth of any hypothesized fault, construct a filter to skeletonize it
Determine if a given voxel is a local fault probability peak
If so, interpolate fault probability, fp, on either side, normal to the local fault plane
Construct a parabola through the probability values at these three points
Find the location and magnitude of the peak of the parabola, smax (in general, not on a voxel!)
Distribute this magnitude about the 8 nearest neighbors using inverse distance weighting

## Slide 40
Seismic amplitude
Coherence
Coherence not only detects faults, but also measure all lateral discontinuities.
Fault anomalies are disconnected. Lateral discontinuities are chaotic.
Faults exhibit the well-known “stair case” artifacts on the vertical slices.
Limitations of coherence fault images
(Courtesy Jie Qi, OU)

## Slide 41
Seismic amplitude
Coherence
Fault enhancement skeletonization result
Limitations of coherence fault images
(Courtesy Jie Qi, OU)
Notes: Stair-step fault artifacts (blue arrows)have been reduced, and anomalies parallel to stratigraphy suppressed.
“Thick” black smears (yellow arrows) correspond to unconformities and condensed sections subparallel to the stratigraphic reflectors

## Slide 42
Determining if a fault plane exists near the analysis point
Step 1: Interpolate values Uleft and Uright
  Assume the center analysis point U14 is at (0,0,0) and the point U1 is at (-dx,-dy,-dz)
U2
U3
U4
U5
U6
U7
U8
U9
U14
U10
U13
U15
U11
U12
U16
U17
U18
U27
U19
U20
U21
U22
U23
U24
U25
U26
Uleft
V3
U1
Uright
(Courtesy Jie Qi, OU)
Notes: Cartoon showing details of directional skeletonization. (a) The analysis window about each voxel consisting of eight sub cubes and 26 neighboring voxels. The green plane indicates a locally planar event with center point . and define points where the eigenvector intersects to the analysis window. The attribute value at is interpolated from the corner values of the red square , , , and . The attribute value at is interpolated from the corner values of the blue square , , , and .
Finding eigenvector 𝒗_𝟑 is key to directionally skeletonize planar anomalies in coherence images. For each voxel, we extract 26 neighboring samples of fault probability that fall within a size of ±𝑑𝑥∗±𝑑𝑦∗±𝑑𝑧 gridded window.
There is a hypothesized plane in green, intersecting the center of the window at point U14. The intersection of 𝒗_𝟑 with this window gives the locations (𝑈_𝑙𝑒𝑓𝑡,〖 𝑈〗_𝑟𝑖𝑔ℎ𝑡) which fall in the 2D red rectangular.
We assume the center analysis point U14 is at (0,0,0) and the point U1 is at (-dx,-dy,-dz).

## Slide 43
Finding the optimum location and value for the fault
Step 2: If Uleft < U14 and Uright < U14 a “fault” falls near the analysis point
Step 3: Fit a parabola to the three points, Uleft, U14, and Uright
Step 4: Find the maximum location and value along vector v3
V3
Fault probability
U14
Uright
Uleft
Umax
Max value
Location of max value
“Fault” dip magnitude
“Fault” dip azimuth
(Courtesy Jie Qi, OU)
Notes: If the value at the center of the analysis window, or , no fault maximum occurs and we set the skeletonized value to be zero. If the value at the center of the analysis window, and , a fault anomaly falls within the window. We fit a parabola of the form:
The maximum value Umax and distance between U14 and location of Umax projection on the eigenvector is
In general, Umax does not fall on the grid point U14, such that we need to distribute the Umax value into the eight neighboring grid points and the weights functions are based on their distance between the Umax and eight neighboring grid points:
If the center of the analysis window, 𝑈_14< 𝑈_𝑙𝑒𝑓𝑡 or 𝑈_14<𝑈_𝑟𝑖𝑔ℎ𝑡, no fault maximum occurs and we set the skeletonized value to be zero.
distance 𝜉_𝑚𝑎𝑥 between U14 and location of Umax projection on the eigenvector 𝒗_𝟑

## Slide 44
Expressing the interpolated fault location and value
Step 5: Compute skeletonized values on 8 neighboring grid points whose weighted average produces the fault probability at the maximum location
Umax
U1
U2
U3
U4
U5
U6
U7
U8
U9
U14
U10
U13
U15
U11
U12
U16
U17
U18
U27
U19
U20
U21
U22
U23
U24
U25
U26
V3
Umax
U13
U11
U12
U14
U15
U17
U18
U16
Notes: In Figure, Umax falls with a sub-cube of the grid analysis window, indicated by the red dashed line.
We compute skeletonized values on 8 neighboring grid points whose weighted average produces the fault probability at the maximum location. Distributed values will be summed, if the values from neighboring analysis window are located on the same grid points. Finally, all skeletonized values on grid points will be output to the skeletonized image.

## Slide 45
Example 1: Gulf of Mexico
-
-
=
=
Original amplitude
SOF amplitude
0.0
0.5
1.0
1.5
2.0
Time (s)
Positive
Negative
0
Amp
Rejected noise
A
A’
A
A’
(Courtesy Jie Qi, OU)

## Slide 46
A
A’
Coherence (original)
Salt dome
Salt dome
MTC
1 mile
t=1 s
(Courtesy Jie Qi, OU)
Example 1: Gulf of Mexico

## Slide 47
Salt dome
Salt dome
MTC
MTC edge
Salt edge
Salt edge
Salt edge
1 mile
A
A’
Directional skeletonization result
t=1 s
(Courtesy Jie Qi, OU)
Example 1: Gulf of Mexico
Notes: Note that faults after our workflow are more continuous, with higher contract. Other noises are rejected after process. Subtle feature that limit in mass transport complexes are also enhanced. Stair step artifacts in the faults have been reduced, and anomalies parallel to stratigraphy suppressed.

## Slide 48
High
Low
Prob
Directional LoG skeletonization result
High
Low
Coh
A
A’
0.0
0.5
1.0
1.5
2.0
Time (s)
Salt dome
Salt dome
Coherence
(Courtesy Jie Qi, OU)
Example 1: Gulf of Mexico
Notes: Note that faults after our workflow are more continuous, with higher contract. Other noises are rejected after process. Subtle feature that limit in mass transport complexes are also enhanced. Stair step artifacts in the faults have been reduced, and anomalies parallel to stratigraphy suppressed.

## Slide 49
Skeletonized fault probability co-rendered with fault dip & azimuth
N
High
Low
Prob
Opacity
High
Low
Mag
Opacity
Azim
Opacity
High
Low
Amp
Opacity
0.0
0.5
1.0
1.5
2.0
Time (s)
Dipping SE
Dipping North
Dipping North
1 mile
N
S
E
W
Dip Mag
Dip Azim
(Courtesy Jie Qi, OU)
Example 1: Gulf of Mexico
Notes: 3D view showing several inlines of the direction skeletonization result co-rendered with seismic amplitude by the Hue-Saturation-Lightness (plotted against a 3D color bar). Faults orientation is readily seen. More organized continuity artifacts now appear within the salt. While such pattern are easily recognized by the interpreter, they could also be marked by an attribute that is sensitive to the internal low amplitude reflectivity common to salt

## Slide 50
N
High
Low
Prob
Opacity
High
Low
Mag
Opacity
Azim
Opacity
High
Low
Amp
Opacity
0.0
0.5
1.0
1.5
2.0
Time (s)
Dipping SW
Dipping SW
Dipping NE
1 mile
N
S
E
W
Dip Mag
Dip Azim
Skeletonized fault probability co-rendered with fault dip & azimuth
(Courtesy Jie Qi, OU)
Example 1: Gulf of Mexico

## Slide 51
0.2
1.7
Time (ms)
Amp
High
0
Low
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 52
1
0.5
Coh
0.2
1.7
Time (ms)
Original coherence
Coherence after footprint suppression
Coherence after SOF
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 53
1
0.5
Coh
0.2
1.7
Time (ms)
Multispectral coherence
After alpha trim mean filter
The residual
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 54
Multispectral coherence after directional LOG
Multispectral coherence after iter directional LOG
Multispectral coherence after Iter energy-weight directional LOG
The residual after 3 iterations of energy-weighted directional LoG
1
0.5
Coh
0.2
1.7
Time (ms)
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 55
Seismic amplitude co-rendered with fault probability
0.2
1.7
Time (ms)
High
Low
Fault
probability
Amp
High
0
Low
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 56
Co-rendered fault probability, dip magnitude, and dip azimuth
0.2
1.7
Time (ms)
Fault
probability
High
Low
Fault
dip magnitude
Fault
dip azimuth
180
-180
90o
0o
Opacity
Opacity
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 57
Coherence
Variance
Fault probability
Corendered fault probability, dip magnitude and dip azimuth
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 58
0.2
1.7
Time (ms)
0.2
1.7
Time (ms)
Automatic fault tracking using ant tracking
Automatic fault tracking using fault probability
0.2
1.7
Time (ms)
0.2
1.7
Time (ms)
Variance followed by Ant Tracking
Fault probability
(Qi, 2018)
Example 2: Taranaki Basin

## Slide 59
(Qi, 2018)
Example 2: Taranaki Basin
Interpreter-picked fault sticks
Extracted surfaces from fault probability

## Slide 60
Desired Discriminator
Cluster 1
Cluster 2
φ
φ
+180°
-180°
There is no single discriminator !
Pitfalls in correlating an engineering or geologic property with cyclical attributes
Notes: The most natural way to define the variation of lithology with direction would be to provide azimuth from an origin as an input attribute. Unfortunately, if the azimuth is defined to range between ±180°, we can not parameterize the problem with a single layer of perceptrons.

## Slide 61
Desired Discriminator
Cluster 1
Cluster 2
φ
Easting (sinφ)
Northing (cosφ)
Construct continuous geodetic attributes N=cosφ and E=sinφ
Correlating an engineering or geologic property with cyclical attributes
Notes: By defining azimuth using two attributes, northing and easting, the problem becomes more easily separable, with a single discriminator being able to correlate desired parameters with any orientation. Similar correlations can be done with North and East components of reflector dip, aberrancy and other cyclical attributes.
Deep neural networks also transform the data, and may be able to figure out that they need to convert azimuths into their north and east components.

## Slide 62
Z (Down)
X (North)
Y (East)
n
a
θ
ψ
Fault plane
Plane defined by the normal and the z-axis.
Discontinuities when defining a fault plane by its dip and azimuth
30°
60°
North
East
90°
Dip magnitude
0°
South
West
+135°
-135°
-45°
+45°
Two problems:
Faults with azimuths ≈-180° and ≈+180° should fall next to each other
Vertical faults with azimuths φ and φ+180° should fall next to each (and have a similar color mapping)
Notes: Because faults are often vertical, the discontinuities associated with dip magnitude and dip azimuth of fault planes are more challenging than those of dipping reflectors which tend to be more horizontal.

## Slide 63
Pitfall: Dip azimuth values flip about vertical faults
Vector display using an HSL color model resulting in polarity flips
2 km
200 ms
t=1.40 s
t=1.32 s
Inline 3101
1.32
1.40
N to S flip
N to S flip
E to W flip
E to W flip
Notes: This image shows a vertical slice and two time slices through what I consider to be a conventional means (OK, the way Marfurt does it!) of displaying the local dip and azimuth of a fault surface. In the yellow box on the time slice and on the time slice at t=1.40 s, note that the fault plane changes orientation from blue (North) to yellow (South). Likewise, in the magenta box, note that the fault on the vertical slice and the time slice at t=1.32 s changes orientation from magenta (Northeast) to cyan (Northwest). Both of these faults are near vertical and the slight “wavering” about the vertical results in a totally different color.

## Slide 64
North strike component: cos(2σ); σ=ψ+90°
2 km
200 ms
t=1.40 s
t=1.32 s
Inline 3101
1.32
1.40
Partial solution: Generate fault orientation components

## Slide 65
East strike component: sin(2σ); σ=ψ+90°
2 km
200 ms
t=1.40 s
t=1.32 s
Inline 3101
1.32
1.40
Partial solution: Generate fault orientation components

## Slide 66
Horizontal dip component: cos(θ)
2 km
200 ms
t=1.40 s
t=1.32 s
Inline 3101
1.32
1.40
Partial solution: Generate fault orientation components

## Slide 67
Vertical dip component: sin(θ)
2 km
200 ms
t=1.40 s
t=1.32 s
Inline 3101
1.32
1.40
Partial solution: Generate fault orientation components

## Slide 68
Image enhancement of faults
In Summary:
By using iterative application of larger analysis windows, image enhancement filters can
  fill in the holes seen in coherence images when unrelated stratigraphic reflectors correlate across a fault, and
  minimize the stairstep artifacts associated with the seismic wavelet being imaged perpendicular to the reflector.
Eigenvectors of the 2nd moment tensor computed from coherence volumes provides
  estimates of fault dip and azimuth, and
  a means to directionally sharpen or smooth the fault
Skeletonization converts diffuse fault edges into sharper surfaces
Fault enhancement is not limited to coherence images, but can be applied to curvature volumes to better map fold axes
Fault enhancement algorithms can also enhance footprint!
Notes: Summary comments on image processing